## Slide 1
Smart Temperature Alert System
IoT201 - Introduction to IoTs
PRESENTED BY
Zaid Ahmed Khazaleh
ID: 188472
Ahmad Radwan Ababneh
ID: 172393

## Slide 2
Why Do We Need Automated Temperature Monitoring?
Temperature-sensitive environments—server rooms, medical storage, greenhouses—require constant monitoring. Manual checks are slow, unreliable, and cannot respond fast enough to sudden changes. A single overheating event can cause thousands of dollars in equipment damage or endanger lives. An automated, real-time alert system is essential.
01
Manual monitoring is inefficient and error-prone
02
Overheating causes equipment failure and safety hazards
03
Real-time alerts enable immediate corrective action
04
Automation reduces reliance on human presence

## Slide 3
Smart Temperature Alert System — Overview
Our system uses an Arduino Uno and a TMP36 temperature sensor to continuously monitor ambient temperature. When the temperature exceeds a defined threshold (30°C), the system immediately activates a Red LED and a Piezo Buzzer to alert nearby personnel. Below the threshold, a Green LED confirms normal operating conditions.
Continuous, real-time temperature monitoring
Instant visual alert: Red LED for danger
Visual confirmation: Green LED for safe
Auditory alarm via Piezo Buzzer at 1000 Hz

## Slide 4
Hardware Components
COMPONENT
QUANTITY
ROLE
Arduino Uno
1
Main microcontroller
TMP36 Sensor
1
Reads ambient temperature
Green LED
1
Normal state indicator
Red LED
1
Alert state indicator
Piezo Buzzer
1
Audible alarm
220Ω Resistors
2
Current limiting for LEDs
All components are standard, low-cost, and available in Tinkercad's simulation library.

## Slide 5
Wiring Diagram and Pin Assignments
The circuit connects the TMP36 sensor to Arduino's analog pin A0 for temperature reading. The Green LED is connected to digital pin 8, the Red LED to pin 9, and the Buzzer to pin 10. Two 220Ω resistors protect the LEDs from excessive current.
Connection Summary
TMP36 VCC → Arduino 5V (Red wire)
TMP36 OUT → Arduino A0 (Purple wire)
TMP36 GND → Arduino GND (Black wire)
Green LED (+) → Pin 8 via 220Ω
Red LED (+) → Pin 9 via 220Ω
Buzzer (+) → Pin 10

## Slide 6
Two-State Finite State Machine Controls All Outputs
The system is a two-state machine. In the NORMAL state (temp < 30°C) the green LED is ON and alarms are silent. In the ALERT state (temp ≥ 30°C) the red LED and buzzer activate. The sensor is polled every second and the machine transitions based on the reading.
NORMAL STATE
Condition: Temp < 30°C
Green LED: ON • Red LED: OFF • Buzzer: OFF
↕
ALERT STATE
Condition: Temp ≥ 30°C
Green LED: OFF • Red LED: ON • Buzzer: ON (1kHz)

## Slide 7
Arduino Code — Clean, Commented, and Readable
The code reads the raw ADC value from pin A0,
converts it to Celsius using the TMP36 formula
(Voltage - 0.5) * 100
, then compares it to
the 30°C threshold. The entire logic runs in a
loop()
function that executes every 1 second.
// Convert raw ADC to Celsius float voltage = rawValue * (5.0 / 1023.0); float tempC = (voltage - 0.5) * 100.0; if (tempC < threshold) { digitalWrite(greenLED, HIGH); } else { digitalWrite(redLED, HIGH); }
setup()
Initializes pins and Serial Monitor
analogRead(A0)
Reads raw sensor value (0–1023)
Conversion Formula
Voltage & Celsius conversion math
if/else block
Controls LED and Buzzer outputs based on threshold
delay(1000)
1-second polling interval for continuous monitoring

## Slide 8
Sensor Calibration and Test Results
The TMP36 sensor has a linear output, making it highly predictable. Four test cases were run in the Tinkercad simulation, covering both normal and alert conditions. All test cases produced the expected outputs without any errors.
LINEAR SCALE FACTOR
10 mV / °C
OFFSET VOLTAGE (AT 0°C)
500 mV
TEST
TEMP (°C)
EXPECTED OUTPUT
RESULT
TC-01
20.0
Green ON
PASS
TC-02
29.5
Green ON
PASS
TC-03
30.5
Red ON + Buzzer
PASS
TC-04
50.0
Red ON + Buzzer
PASS

## Slide 9
System Limitations
While the current prototype successfully demonstrates automated temperature monitoring, it has specific architectural limitations that must be addressed before it can be deployed in a real-world industrial environment.
HARDCODED THRESHOLDS
The 30°C alert limit is fixed directly within the Arduino code. Changing this threshold requires modifying the source code and reprogramming the microcontroller, which is impractical for end-users.
LACK OF HYSTERESIS
The system uses a strict ≥30°C cutoff. If the ambient temperature fluctuates rapidly between 29.9°C and 30.1°C, the alarms will rapidly toggle on and off (chattering), causing hardware wear and user annoyance.

## Slide 10
Next Steps & Conclusion
FUTURE IMPROVEMENTS
01
LCD Display Integration
Add an I2C LCD screen to display real-time temperature readings locally without needing a Serial Monitor.
02
Software Hysteresis
Implement a hysteresis band (e.g., ±1°C) in the code to prevent the alarm from rapidly toggling when hovering exactly at 30°C.
03
IoT Connectivity
Upgrade to an ESP8266 or ESP32 microcontroller to send email or SMS alerts to administrators when thresholds are breached.
CONCLUSION
The Smart Temperature Alert System successfully demonstrates a reliable, automated approach to environmental monitoring.
By utilizing standard Arduino components and a simple finite state machine, the project provides an effective foundation that can be easily scaled for industrial or commercial applications.